## Slide 1: EMON Data Processing (EDP) Tool

## Slide 2: EDP Features
  Supports both steady state and non-steady state workloads
  Supports many architectures
    NHM/WSM EP, NHM/WSM EX, SNB-EP, SNB Client, Atom
  Predefined set of events containing all core and uncore events that are needed for basic characterization
    CPI, branch mispredicts, TLB MPI, L1/L2/L3 MPI, QPI and memory b/w, snoop events
    Thread/core/socket level view for all the metrics
  Flexibility for the users to add events of their interest (that are not already in the list)
  XML file that contains formula for all the important metrics
    Easy to maintain and users can also add their own
  Automatic time-series charting of events and metrics
    Shows how events/metrics vary over time
  Various statistical metrics on the emon data
    average, min, max, 95th percentile and variance for all the samples collected
Highly customizable and easy to support

## Slide 3: How to use EDP
  Collect EMON data on the target system
    Either the data could be collected over the entire duration of the workload execution
      Emon –stop command can be executed anytime to stop the EMON data collection.
    Or, data could be collected over a specific period of the workload execution (more suitable for steady state execution)
    The collection could be either on Windows or Linux o/s
  Post-process the data on any windows system
    Done through scripts based on Ruby scripts
    Parallelizes the processing if there are more h/w threads available on the system
    Automatically imports the data into excel and creates necessary charts

## Slide 4: How to use EDP (contd)
  Drilling down into specific phases
    Typically, the initial data collection is over the entire duration of the workload execution (which includes ramp-up and ramp-down phases)
    Now analyze inst_retired and cpu_clk_unhalted cycles charts for periods of interest and note down the starting and ending sample numbers of those periods
    Modify the jprocess.cmd to select the correct BEGIN and END sample numbers based on the data from previous step
    Re-process the data
      Now the metrics and the charts will be shown for the duration selected
    These steps can be repeated many times for various phases in the workload

## Slide 5: EDP ZIP file package contents
  edp-v*.zip
    readme.docx
      Describes the EDP Tool in detail and how to customize it
    edp.rb
      A Ruby script that processes the EMON raw data and creates a spreadsheet with charts and metrics
    Architecture Specific
      Sub-folders for NHM/WSM-EP, NHM/WSM-EX, SNB-EP and Atom
      Each sub-folder contains 3 files that are specific for that architecture
        <arch_name>-events.txt : Emon events
        <arch_name>.xml : Formulas for deriving the metrics
        chart_format_<arch_name>.txt : Metrics/events for charting in excel
    jprocess.cmd
      A cmd file that drives ruby script
      Implements support for parallelizing the input file processing
      Also used for configuring input/output file names
      process.cmd is the original non-parallel version

## Slide 6: EDP – Basic emon events
  <arch_name>-events.txt:
    Event file: 5 sample groups in WSM-EP : Each event sampled for 100 msec
      Sampling rate is workload dependent and may have to be reduced from 100 msec if workload is bursty (but may add to perturbation);
    Contains 20 core events and many uncore events to cover IMC, QPI and snoop events
-q -k -t0.2 -l100000
-C(
INST_RETIRED.ANY,
CPU_CLK_UNHALTED.THREAD,
CPU_CLK_UNHALTED.REF,
OFFCORE_REQUESTS_OUTSTANDING.DEMAND.READ_DATA,
OFFCORE_REQUESTS.DEMAND.READ_DATA,
BR_INST_RETIRED.ALL_BRANCHES,
BR_MISP_RETIRED.ALL_BRANCHES,
UNC_IMC_NORMAL_READS.ANY,
UNC_IMC_WRITES.FULL.ANY,
UNC_LLC_MISS.ANY,
UNC_LLC_LINES_OUT.M_STATE,
UNC_IMC_NORMAL_OCCUPANCY.ANY,
UNC_QHL_REQUESTS.IOH_READS,
UNC_QHL_REQUESTS.IOH_WRITES,
UNC_QPI_HCLK_TX_PACKETS.PROTOCOL.LINK_0,
UNC_QPI_HCLK_TX_PACKETS.PROTOCOL.LINK_1,
UNC_CLOCKTICKS,
INST_RETIRED.ANY,
CPU_CLK_UNHALTED.THREAD,
CPU_CLK_UNHALTED.REF,
OFFCORE_RESPONSE_0.ANY_IFETCH.ANY_LLC_MISS,
L2_RQSTS.PREFETCH_MISS,
L2_RQSTS.PREFETCHES,
L2_WRITE.RFO.I_STATE,
UNC_IMC_NORMAL_READS.ANY,
UNC_IMC_WRITES.FULL.ANY,
UNC_LLC_MISS.ANY,
UNC_LLC_LINES_OUT.M_STATE,
UNC_QHL_REQUESTS.REMOTE_READS,
UNC_QHL_REQUESTS.REMOTE_WRITES,
UNC_QHL_REQUESTS.LOCAL_READS,
UNC_QHL_REQUESTS.LOCAL_WRITES,
UNC_QPI_HCLK_CLOCKTICKS:ALL,
3 fixed counter events present in every group
4 events focusing on core/L1/L2 events in every group
Memory b/w events are present in every group for complete coverage

## Slide 7: EDP - Derived metrics
  Formulas for computing all the metrics are defined in <arch_name>.xml file
    Can contain references to events that are not collected
      Metrics will be computed only for events for which samples are present
    Can add your own metrics
<metric name="metric_CPI">
<event alias="a">CPU_CLK_UNHALTED.THREAD</event>
<event alias="b">INST_RETIRED.ANY</event>
<formula>a/b</formula>
</metric>
<metric name="metric_memory_bandwidth_total (MB/sec)">
<event alias="a">UNC_IMC_NORMAL_READS.ANY</event>
<event alias="b">UNC_IMC_WRITES.FULL.ANY</event>
<formula>(a+b)*64/1000/1000</formula>
</metric>
Examples of metrics from WSM-EP.xml

## Slide 8: EDP – Charts for metrics/events
  chart_format_<arch_name>.txt
    Specifies what & how you want the data charted (#Columns separated by blank line)
    Names listed together in adjacent lines are charted side-by-side
    A blank line puts the next group in a new row
CPU_CLK_UNHALTED.THREAD
CPU_CLK_UNHALTED.REF
metric_CPU_utilization_%
INST_RETIRED.ANY
metric_CPI
metric_mispredict_ratio
metric_L2_Any local request that HITM in a sibling core (per inst)
metric_L2_Core sends HITM response to snoop (per inst)
metric_L2_read_miss_latency(in core clocks)
Examples from chart_format_wsm_ep.txt
Charts for these three metrics appear side-by-side

## Slide 9: EDP – Process.cmd script
  process.cmd: Cmd file to post-process the raw data
    @echo off
    :: ruby interpreter, change it according to the path where ruby is installed in your system
    set RUBY="ruby.exe"
    :: input file names, you may need to change them
    set EMON_DATA=emon.dat
    set EMON_V=emon-v.dat
    set EMON_M=emon-m.dat
    :: output file name, you may want to change it
    set OUTPUT=summary.xlsx
    :: the metrics definition file; need to change this based on the architecture
    set METRICS=wsm-ep.xml
    :: Excel chart format file, Need to change it based on the architecture
    set CHART_FORMAT=chart_format_wsm_ep.txt
    :: the average value will be calculated from the %BEGIN% sample to %END% sample.
    :: setting %END% to a negative value means the last available sample.
    set BEGIN=1
    set END=100000
    ::set BEGIN=1
    ::set END=-1
    :: QPI frequency in GT/sec
    :: QPI frequency cannot be detected automatically, so user needs to specify it manually.
    set QPI=6.4
    :: by default only system view will be outputted
    :: there are 3 optional views to be selected
    :: you can select one or more of them
    set VIEW=--socket-view
    ::set VIEW=--socket-view --core-view --thread-view
    ::set VIEW=
    ::set the throughput (Transaction per Second)
    ::set TPS=--tps 10
    %ruby% edp.rb -i %EMON_DATA% -j %EMON_V% -k %EMON_M% -f %CHART_FORMAT% -o %OUTPUT% -m %METRICS% -b %BEGIN% -e %END% -q %QPI% %VIEW%
EMON data file names collected from the target server
Sample range of interest for deeper drill-down
Drilling down data into socket/core/thread views
Transactions per second

## Slide 10: EDP – Jprocess.cmd script
:: ruby interpreter, change it according to the path where ruby is installed in your system
set JRUBY="jruby.exe"
set RUBY="ruby.exe“
:: JVM options for JRuby.
:: --server means using server JVM, which means better GC efficiency
:: 5g is the heap size, a larger heap size is always helpful.
set JRUBY_OPTIONS=--server -J-Xmx5g -J-Xms5g --1.8
:: number of threads to process data in parallel. Typically it should equal to the number of logical CPUs in your processing system.
set PARALLELISM=24
:: input file names, you may need to change them
set EMON_DATA=emon.dat
set EMON_V=emon-v.dat
set EMON_M=emon-m.dat
set VIEW=--socket-view
::set VIEW=--socket-view --core-view --thread-view
::set VIEW=
::set the throughput (Transaction per Second)
::set TPS=--tps 10
%JRUBY% %JRUBY_OPTIONS% edp.rb -i %EMON_DATA% -j %EMON_V% -k %EMON_M% -f %CHART_FORMAT% -o %OUTPUT% -m %METRICS% -b %BEGIN% -e %END% -q %QPI% %VIEW% %TPS% --step 1 -p %PARALLELISM%
%RUBY% edp.rb -i %EMON_DATA% -j %EMON_V% -k %EMON_M% -f %CHART_FORMAT% -o %OUTPUT% -m %METRICS% -b %BEGIN% -e %END% -q %QPI% %VIEW% %TPS% --step 2
Number of parallel threads
J-ruby used to split EMON input file and process in parallel with multiple threads
Excel charting is still done with single thread due to bugs w/ Jruby
  jprocess.cmd: super-set of process.cmd with support for parallel processing